Requirements and design: RD002 v0.2 Mobile Application_od.odt
Application name:	Mobile Application

Table of Contents

# Introduction
## Purpose
This document serves as a foundation for the development of the mobile application of MaGeX project. It contains requirements specifications that define the capabilities of the application. Based on these requirements individual modules of the application are designed. These designs define interfaces between modules.
## Application description
Mobile application is the base part of MaGeX project. Its purpose is to display maps stored in a mobile phone, combine them with user data as a separate map layers and with GPS data.
Description of the MaGeX project and its individual applications and their interaction is described in document RD001.
## Terminology
This document contains tables with requirements using words and phrases that command the presence of some feature, function or deliverable. They are to be interpreted in the following way:
shall or shall not – used to dictate the provision of a functional capability
- must or must not – used to establish performance requirement or constraint
- is required to – used as an imperative when written in passive voice
- are applicable – used to include, by reference, standards, or other documentation as an addition to the requirement being specified
- will – used to cite things that the operational or development environment is to provide to the capability being specified
- should – used to define optional capability that is preferred to be included
- may – used to define optional capability
## Design
This document contains tables describing interfaces and configuration properties. This information will be used during development, to synchronize between developers.
### Interfaces
Each interface table contains methods of one specified class. Description of each method contains method parameters and its return value type.
### Configuration properties
Each configuration properties table contains properties of one specified class. This class implements get and set methods for each property. These properties will be configurable by common user interface, described in chapter 7.
## Overview of the following document
Chapter 2 starts with common features used throughout the mobile application. Then, chapter 3 defines requirements for data storage, describes data formats and interfaces for other modules to work with stored data. Next, chapter 4 presents functionality of providing GPS data for the rest of the modules. In chapters 5 and 6, communication with server application and with data transfer application and other mobiles is defined. Finally, chapter 7 deals with the user interface.
# Common features
## Exception handling
All modules in the mobile application will use common exception handler. This handler will process all exception classes defined in this document.

Interface – ExceptionHandler
Method	Description	Parameters / Return value

## Bluetooth communication
Mobile application uses Bluetooth protocol to communicate with GPS devices, desktop applications and other mobile applications. All these functions require the same communication actions – search for available devices, service enumerations, user selection and connection establish. To unify this process common Bluetooth interface will be created and used in other modules of the application.

# Data storage
## Overview
The application will to store the maps, waypoints and tracks. It shall provide an unified interface for all classes that need to access stored data. The storage methods will be optimized for speed, when keeping size in mind.
### Storage system
The unified storage interface, represented by the StorageSystem class, will serve to retrieve all map and index data stored in the RMS and JAR and store and retrieve any track and waypoint data, saved by the user. The storage system will keep an index record in the RMS, which will contain the list of all records currently stored. The application JAR file must contain an index file, listing all embedded maps, which the storage will then use.
A set of high-level functions will be provided for normal usage, as well as a set of low-level raw data operations in order to access maps and retrieve/send them from/to the desktop application.
The storage system will be able to handle requests for map data from several threads and will avoid sharing violation. All the threads that access the storage system will be required to use a special identification to prevent this. Access to waypoint and track storage will be sequential only.

Requirements
ID	Description	Remark
FR1	Mobile application shall be able to access data stored in JAR file of the application and data stored in record stores using Record Management System (RMS).
FR2	Mobile application shall be able to add, modify and delete data stored in RMS.
FR3	Upon request, the storage system will be able to list all the available maps and all the stored tracks and waypoints and provide means of accessing them directly.	to User interface chapter
FR4	The storage system shall be able, given a map (track) identification, to return all available meta-information, regarding this map (track).
FR5	The storage system shall be able to provide all waypoints, that were previously stored by the user.
FR6	Given a map identification, the storage system shall be able to provide means of accessing its POI index, as well as single records within it.
FR7	Given a map specification, depth level and square division coordinates, the storage system shall provide means of accessing vector map data related to the specified location.
FR8	The storage system class shall throw an appropriate exception, in case any error occurs when reading or writing to the storage.

## Vector map storage
### Overview
The application will store vector maps in RMS as well as use embedded ones in the JAR file. The map consists of points of interest (POI), polygon lines (polylines) and polygons. In addition to this, a map contains a Trie-like index for the application to be able to search within POIs by name. The unified storage system will be used to store, retrieve and delete the map and index data. The map data (POIs, polylines and polygons) shall be split into several JAR files or RMS records, according to the level of detail and their actual location in the map. The index will be split into several JAR files or RMS records as to fit the memory limits of the mobile device's heap.
The mobile application will obtain all the data in the specified formats from the desktop application. No data transformations will be done on the side of the mobile application.
Requirements
ID	Description	Remark
FR9	Mobile application shall be able to store vector maps. These maps are created from POIs, polylines and polygons and may have more than one level of detail.
FR10	The mobile application shall be able to selectively load the relevant map data files, according the to the map coordinates being currently displayed.
FR11	The mobile application shall be able to store a map's POI search index.
FR12	The mobile application shall be able to search within the map's Object index (which shall contain entries for any POIs, Polygons and Polylines that have a label) by name of an object. It shall be able to return up to a fix number of results and then display the relevant location for the selected one, in a relevant level of magnitude.	Max. 100 results?
FR13	The mobile application shall be able to search within map objects by their type and distance from the current location.	No guarantee of speed on this kind of search
FR14	If the mobile device's RMS memory capabilities permit, the mobile application shall be able to store additional map data, which may be downloaded via Bluetooth from the desktop application.

### Data format
The map shall be split to several files record, as to provide faster speed of loading and comply with the memory limits of the mobile devices. One map shall consist of the following files or records:
Map files – list
Name	Description	Remark
ID.meta	All the meta-information about the map
ID.PARTNO.x	Index file part
ID.D.X.Y.d	The actual map data, a part, based on depth level and location

In the previous table, all the uppercase filename strings, which serve as wildcards, are to be replaced as follows:

Map file naming
String	Replacement	Remark
ID	The (short) name of the map, an application-wide unique number for each map.
PARTNO	Part number of the index file, 4 hexadecimal digits. The file with PARTNO = 0000 shall be always present and contain the root of the index.
D	Depth level of the map, 1 hexadecimal digit.
X	X-coordinate of the upper-left corner of this (square) part of the map. Given as the 100000-multiple of the value in degrees, as an 8-digit hexadecimal number
Y	Y-coordinate of the upper-left corner of this (square) part of the map. Number format same as with X.

The ID.meta file shall have the following data format (all Strings are 2byte-length prefixed UTF-8 Strings):
ID.meta – file format
Length	Type	Description
4 B	int	The map ID
variable	String	The map full name
4 B	int	Upper-left corner of the area covered by the map – X coordinate (100000-multiple of the value in degrees)
4 B	int	Upper-left corner of the area covered by the map – Y coordinate
4 B	int	Lower-right corner of the area covered by the map – X coordinate
4 B	int	Lower-right corner of the area covered by the map – Y coordinate
1 B	byte	Number of depth levels
8 B * number of levels	int []	For each level, X and Y size of one map square (in 100000-multiple of the value in degrees)
4 B	int	The total size of all the files, contained in the map (except for maps that are embedded in the JAR file, for which this should be always -1).

No zoom level information should be needed, as long as square sizes are provided.

The D.X.Y.d file shall consist of a list of records, each one representing a single POI, polyline or polygon. The coordinates of the objects shall fall within the range, specified by the coordinates of the upper-left corner (given in the file name) and the size of the cell (given in map header for the depth level, specified in the file name). The objects shall be sorted by their data type (POIs first, then polygons and polylines) and object type.
The format of one record shall be as follows:
D.X.Y.d record format
Length	Type	Description
1 B	byte	Level (upper 4 bits) + Data type (see constants, lower 4 bits)
2 B	char	Object type (according to the object type constants in the definition of the Polish map format)
variable	String	Object name
1 B	byte	Number of coordinates to follow (polyline / polygon only, since for POIs it's always 1)
8 * number of coordinates	int []	X and Y coordinates of all the points involved in the object, given in 100000-multiplies of the values in degrees.

String means 2-byte length prefixed UTF-8 String.

 Object type constants, used in the D.X.Y.d record will be as defined in MapObject (see section 2.2.1).

The indexes shall have a Trie-like tree format. The tree shall consist of inner nodes and leaves, which are to be connected by direct file offsets pointing to the other nodes. The file shall be split to parts, each of them will be smaller than 64 KB, so the 4-byte offset will consist of 2 bytes part number and 2 bytes intra-file offset. No node shall overlap the file boundary.

The format of the inner nodes will be following:
POI search index – inner node format
Length	Type	Description
1 B	0..255	Number of child nodes – must be greater than 1. 0 is a valid value for leaves.
6 B * number of child nodes	{ char, int } []	List of next characters in the child nodes and their offsets. Offset is an absolute 2 + 2 byte value (part number + intra-file offset)

The format of the leaves will be as follows:
POI search index – leaf format
Length	Type	Description
1 B	0..255	Always zero – used to indicate a leaf
variable	String	Rest of the object name (all the chars following the prefix, which is given by the tree path to this leaf)
2 B	char	Object type (according to the Polish format definition)
4 B	int	X-coordinate, in 100000-multiply of the degrees value
4 B	int	Y-coordinate, in 100000-multiply of the degrees value

String is a 2-byte length prefixed UTF-8 string.
### Storage classes
A special data class MapObject will be used by the application to exchange vector map data between its parts. Its content will be accessible directly through the member names. It shall consist of the following:

Members – MapObject
Member	Data type	Description
name	String	The name of the object.
dataType	byte	The actual data type of the object (POI / polyline / polygon).
objectType	char	The object type, according to the Polish format specifications.
points	byte	Number of coordinates, belonging to this object.
coordsX	int []	The X-coordinates of the object (for POI, only the 1st one is valid, for others, only the first points ones are valid).
coordsY	int []	The Y-coordinates of the object (validity same as X-coordinates).

The MapObject class will use the following constants, in order to describe the data type of the object:
Constants – MapObject
Type	Value	Name	Description
Data type	0 POI “This object is a POI” / 1 POLYLINE “This object is a polyline” / 2 POLYGON “This object is a polygon”

Stress shall be put on the reusability of the individual instances and avoiding memory fragmentation while working with them.

The MapInformation class shall be used to store the map meta-information. It will have the following members:

Members – MapInformation
Member	Data type	Description
id	int	The map ID.
String	name	The map name.
boundLeft	int	X-coordinate of the top-left map corner.
boundTop	int	Y-coordinate of the top-left map corner.
boundRight	int	X-coordinate of the bottom-right map corner.
boundBottom	int	Y-coordinate of the bottom-right map corner.
zoomLevels	int	Number of zoom levels.
squareSizesX	int []	Square horizontal sizes for each individual zoom level.
squareSizesY	int []	Square vertical sizes for each individual zoom level.
isInRS	boolean	If true, the map is stored in the RecordStore and therefore may be deleted.
fileSize	int	The total uncompressed size of all the map files, including indexes. This member is valid only for maps contained in RecordStore.

### Searching interfaces
All the search functions within the map will be provided by the MapSearch class. Its instances shall be created in order to search within one map.

Interface – MapSearch
Method	Description	Parameters / Return value
MapSearch	Constructor	int mapId
findByName	Searches for an object with the name that corresponds to the given prefix.	String prefix / / int
findByNameAndType	Searches for an object, given its name’s prefix and a type restriction – only the object types(according to the Polish format specification) listed in the array shall be searched for.	String prefix / char [] types / / int
findByLocationAndType	Searches for objects of given type (according to the Polish format specification), that are near to given coordinates.	char type / int coordX / int coordY / int maxDistance / / int

All search methods return the number of objects found. The actual results data are then placed in the results member. If number of results is greater than the FIND_MAX constant, some results are not returned. The application shall inform the user about this actuality.

If no object meets the given criteria, the methods shall return zero.

Constants – MapSearch
Type	Value	Name	Description
Search limit	100	FIND_MAX	Maximum number of results that the MapSearch class will return.

Members – MapSearch
Name	Type	Description
results	MapObject [FIND_MAX]	Used to store and access the results of the last search. The results are overwritten during the next search.

## Waypoint storage
### Overview
It will be possible to store any position, defined by the user, as a waypoint. The user will be able to add label and description to waypoints. Waypoints will use the internal storage system.

Requirements
ID	Description	Remark
FR15	Mobile application shall be able to store a defined position as a waypoint. Position shall be specified as a point in a map and as a current position. Along with the position, its name and elevation shall be stored.

### Data format
The waypoints shall be stored sequentially using the unified storage system (and may be indexed). Their data format shall look as follows:

Waypoint data format
Length	Type	Description
variable	String	Description of the waypoint
8 B	int [2]	Coordinates of the waypoint (longitude first)
4 B	int	Waypoint elevation.
4 B	int	Waypoint type (according to the Polish format definition)
8 B	long	Waypoint creation time

The actual name of the waypoint, along with its position in the waypoint record (that shall serve as its ID), shall be stored in the waypoint index file, which shall contain records in following format:

Waypoint index-file data format
Length	Type	Description
variable	String	Name (label) of the waypoint
4 B	int	Waypoint ID, i. e. position of the waypoint data in the waypoint record.

### Interface
The interface for reading / writing waypoints from / to the storage interface will correspond to the data format:
Interface – Waypoint
Method / variable	Description	Parameters / Return value
Waypoint	Constructor	String label
String label	Name of waypoint (may be null!).
String legend	Description of the waypoint.
int coordX	Longitude of the point.
int coordY	Latitude of the point.
int elevation	Waypoint elevation.
int waypointType	Type of the waypoint (types as for POI possible).
long time	Creation time.

## Track storage
### Overview
The user shall be able to record tracks – sequences of coordinates recorded through their journeys. They will be stored automatically using current position information from the GPS module.

Requirements
ID	Description	Remark
FR16	Mobile application shall store information retrieved from a GPS module. This shall be done in a form of a track – a sequence of coordinates.
FR17	Coordinates in a stored track shall be stored in regular intervals. If the application alters the track in a way that the intervals between the coordinates will not stay the same (e.g. it deletes a coordinate), it shall store a time difference between coordinate that build up the track.

### Data Format
The tracks shall be stored using the unified storage system, too, and indexed. Their data format shall look as follows:

Track data format
Length	Type	Description
variable	String	Description of the track
4 B	int	Number of coordinates
4 B	int	Length of the track in centimeters
8 B	long	Time for the first coordinate
16 B * number of coordinates	{int, int, int, int} []	Latitudes, longitudes, elevations and time differences from the first (in this order) for all the track coordinates.

Similarily to the waypoints, the tracks' names shall be stored in the track index file only. The structure of the index file with be the following:

Track index-file data format
Length	Type	Description
variable	String	Name (label) of the track
4 B	int	ID of the track, i. e. the number of the actual record the track is stored in.

### Interface
The interface of the Track class, which will represent a track in the application's memory, will correspond to the storage data format, but reflect the assumed way of usage:

Interface – Track
Method / variable	Description	Parameters / Return value
Track	Constructor	String label
getLength	Computes the length of the track in centimeters.	/ int
String label	Name of the track (may be null!).
String legend	Description of the track.
int length	Length of track. Set once after saving from getLength method.
Vector <int> coordsX	Vector of longitudes of all coordinates.
Vector <int> coordsY	Vector of latitude of all coordinates of the track.
Vector <int> elevations	Vector of elevation of all coordinates of the track.
Vector <long> times	Vector of time of all points of track.

## Interfaces
### StorageList
For several operations, regarding the retrieval of a list of objects (maps, tracks, waypoints) with their names and identification, a special class named StorageList shall be used. It shall contain following members:

Members – StorageList
Member	Data type	Description
names	String []	Names of all the objects
ids	int []	ID numbers for all the objects, that shall be used in all further operations with them.

### StorageSystem
The StorageSystem class itself shall use the following interface:
Interface – StorageSystem
Method	Description	Parameters / Return value
StorageSystem	Constructor	-
getAvailableMemory	Returns the maximum amount of memory, that is currently available for storing maps, tracks and waypoints. No guarantee of reliability of this value – it's just for one RecordStore, and we shall use more of them!	- / long
getAvailableMaps	Returns list of available maps (their identification)	- /StorageList
getMapInformation	Returns map meta-information	int mapId / / MapInfromation
getRawMapData	Returns map data (directly as DataInputStream) for the specified depth and location	int mapId int depth int coordX / int coordY / DataInputStream
openMapData	Reserves and opens the map data file that corresponds to the specified location for consecutive high-level operations in the current thread. Returns a handle number that must be provided as a parameter for all operations.	int mapId / int depth / int coordX / int coordY / / int
closeMapData	Ends the work with a map data file. MUST be called in order to keep memory usage etc. down.	int handle / / void
getMapData	Fills the data parameter with the next object in the part of the map specified by the handle , returns true if successful.	int mapIdint handleMapObject data / / boolean
getRawMapIndex	Returns a specified part of the given map's POI search index	int mapId / int partNo / / DataInputStream
addMap	Adds new map (metaInfo parameter must contain the map meta-information data in the prescribed format )	int mapId / byte [] metaInfo / / void
addMapData	Adds data to the map (only after a map has been added)	int mapId / int depth / int coordX / int coordY / byte [] data / / void
addMapIndex	Adds POI index data to the map (only after a map has been added)	int mapId / int partNo / byte [] data / / void
deleteMap	Completely deletes all the data of the given map. The map must be stored in RMS.	int mapId / / void
getRawWaypoints	Returns all the stored waypoints (raw data)	/ DataInputstream
getAvailableWaypoints	Returns the list of all stored waypoints (their identification).	- / StorageList
getWaypoint	Returns a waypoint (given its identification).	int waypointId / / Waypoint
addWaypoint	Stores a new waypoint, returns its identification.	Waypoint waypoint / / int
addRawWaypoint	Stores a new waypoint (raw data in the prescribed format).	byte [] waypointData / / void
deleteWaypoint	Deletes a waypoint from the RMS	int waypointId / / void
getTracks	Returns a list of all stored tracks (their identification)	/ StorageList
getRawTrackData	Return the raw data, belonging to a specified track	int trackId / / DataInputStream
getTrack	Returns a track (given its identification)	int trackId / / Track
addTrack	Stores a new track, added by the user. Returns the identification of the new stored track.	Track track / / int
addRawTrack	Stores a new track (raw data in the prescribed format).	byte [] trackData / / void
deleteTrack	Deletes a track from the RMS	int trackId / / void

All of the methods described in the previous table may throw the StorageSystemException, with appropriate exception code. The exception class is defined as follows:

Interface – StorageSystemException
Method	Description	Parameters / Return value
StorageSystemException	Constructor	int code
getCode	Returns the exception code	/ int

Interface – Constants
Type	Value	Name	Description
Exception code	0 OK No error. / 1 INVALID_OBJECT The object with the specified name does not exist. / 2 EXISTS The specified object name is already being used. / 3 OUT_OF_MEMORY Data write error: out of memory. / 4 WRITE_ERROR general data write error / 5 READ_ERROR Data read error (invalid file format).

# GPS communication
## Overview
Mobile application will support multiple types of GPS devices. To simplify working with GPS data from other modules of the application a general GPS module interface will be implemented.
## General
### Overview
Following text defines general GPS module interface.

Requirements
ID	Description	Remark
FR18	Mobile application shall be able to communicate with GPS devices and use data provided by them.
FR19	Mobile application shall be able to provide the following information retrieved from GPS devices: current position, speed, course, altitude, time and horizontal and vertical accuracy.
FR20	Mobile application shall work even without a working GPS device. Functionality that does not depend on GPS data shall not be altered or disabled.

### Interfaces
GPSProvider is needed to use GPS device’s services and must be created before using any GPS service.

Interface – GPSProvider
Method	Description	Parameters / Return value
GPSProvider	Constructor	int type (NONE, LAPI)
GPSProvider	Constructor	int type (BLUETOOTH, SERIAL) / InputStream in / OutputStream out
GPSProvider	Constructor	int type (SIMULATOR) / long simulatorCenterX / long simulatorCenterY / long simulatorRadius / int simulatorSpeed
getGPSLocation	Returns a	/ GPSLocation
getState	Returns GPS device state	/ int GPS STATE
reset	Resets the provider	-
addLocationListener	Registers a listener	GPSListener listener / int interval / int maxAge
removeLocationListener	Unregisters a listener	GPSListener listener

The GPSLocation provides info about the actual position.

Interface – GPSLocation
Method	Description	Parameters / Return value
GPSLocation	Constructor	-
getLatitude	Returns the latitude in degrees / Positive values for northern and negative for southern latitude.	/ double latitude
getLongitude	Returns the longitude in degrees / Positive values for eastern and negative for western longitude	/ double longitude
getAltitude	Returns the altitude in meters above The Reference ellipsoid	/float
getCourse	Returns course in degrees, multiplied by 100.	/ int
getSpeed	Returns the speed in m/s	/ int
getTimestamp	Returns timestamp of provided info	/ long
getGPSType	Returns GPS provider’s type	/ int type
isValid	Returns if actual info are correct	/ boolean
getSatellitesInView		/ int
getSatellitesUsed		/ int
getPrecision		/ int

An object that wants to use GPS must implement GPSListerner and register itself at GPSProvider.addLocationListener(). These listeners are notified about changes in time period of specified as interval parameter.
Interface – GPSListener
Method	Description	Parameters / Return value
locationUpdated		GPSProvider provider / location
providerStateChanged		GPSProvider provider / int newState

Interface – GPSException
Method	Description	Parameters

Interface – Constants
Type	Value	Name	Description
GPS state	0 OUT_OF_SERVICE No GPS device can be found. / 1 TEMPORARILY_UNAVAILABLE GPS device available, but no data available. / 2 AVAILABLE GPS data available.
GPS type	0 GPS_NONE / 1 GPS_LAPI / 2 GPS_SERIAL / 3 GPS_BLUETOOTH / 4 GPS_SIMULATOR

### Required configuration properties
Configuration properties – GPSProvider
Item	Description	Property
GPS type	Type of GPS device. Possible values: None, Location API, Serial, Bluetooth, Simulator.	int GPStype

## Location API
### Overview
General GPS module interface is derived from Location API (JSR 179) interface. Implementing this interface is merely wrapping its methods. Some of the functionality is simplified.

Requirements
ID	Description	Remark
FR21	Mobile application shall be able to communicate with GPS devices using Location API (JSR 179).

### Connection
create an provider instance, register a listener.
### Required configuration properties
No configuration is required.
## Serial
### Overview
usually internal device, passive communication

Requirements
ID	Description	Remark
FR22	Mobile application should be able to communicate with GPS devices using a serial port and NMEA 0183 protocol.

### Connection
Mobile application will use StreamConnection class and establish a connection using open("comm:port;baudrate=4800"). It will then open an input stream and read data from it in a loop.
### Data format
Communication with GPS device will be done using NMEA 0183 protocol. Sentences supported by mobile application are described in chapter 4.7.
## Bluetooth
### Overview
regular device discovery, then similar routines as serial

Requirements
ID	Description	Remark
FR23	Mobile application shall be able to communicate with GPS devices using Bluetooth and NMEA 0183 protocol.

### Connection
find available devices, select one, open port
try to connect to predefined device?
Mobile application will use ... and establish a connection and open an input stream and read data from it in a loop.
### Data format
Communication with GPS device will be done using NMEA 0183 protocol. Sentences supported by mobile application are described in chapter 4.7.
### Required configuration properties
will need any? predefined device?
## Simulator
### Overview
useful for testing – development and maps

Requirements
ID	Description	Remark
FR24	Mobile application should offer a user an internal GPS device simulator.

### Patterns simulated
circle, clockwise direction
### Required configuration properties
Configuration properties – GPSProvider
Item	Description	Property
Center position	Position of the circle center used to simulate GPS device.	long simulatorCenterX / long simulatorCenterY
Radius	Radius in meters of the circle center used to simulate GPS device.	long simulatorRadius
Speed	Speed in m/s used to simulate GPS device.	int simulatorSpeed

## NMEA sentences
The NMEA 0183 standard specifies communicating parameters between marine electronic devices such as GPS devices. The standard uses a simple ASCII, serial communications protocol that defines how data is transmitted in a sentence from one talker to one listener at a time. Serial configuration uses baud rate of 4800, 8 data bits, no parity and 1 or more stop bits.
Each message from a GPS device starts with a dollar sign and letters “GP”. Next three characters identify the type of the message, followed by data fields separated by commas. Last data field is followed by an asterisk and two-hex-digit checksum. Checksum is calculated as XOR of all characters between the dollar sign and the asterisk; it will not be checked by the application. Each sentence is ended by CR/LF characters.
Following text lists all supported sentences and describes how they are handled.
### RMC – Recommended minimum data for GPS
After receiving this message GPSProvider will store the data into its properties and call locationUpdated method of all registered location listeners.
### GCA – Fix information

### GSA – Overall Satellite data

### GSV – Detailed Satellite data

# Communication with the server
## Overview
Mobile application will communicate with the server application to send its current position and to retrieve position of other users. Apart from this, mobile phones running this application may be used to track moving vehicles. Functionality required for all these tasks is described in the following text.

Requirements
ID	Description	Remark
FR25	Mobile application shall be able to send the information returned by a GPS device to the server application. This information shall include user’s current position, speed and altitude.
FR26	It shall be possible to send the information once and continuously in defined time interval.
FR27	Mobile application shall allow the user to receive information about other users from the server application.
FR28	Mobile application shall allow the user to specify which users are allowed to receive his/her position information.
FR29	Mobile application should be able to automatically start sending GPS information when the current position is more than a predefined distance from predefined position.
FR30	If the mobile application fulfills FR29, it shall be able to process requests sent from the server, once it starts sending GPS information.
FR31	If the mobile application fulfills FR30, it shall be able to stop sending GPS information upon request. This request shall include a time period for which the mobile application will cease to send the data.
FR32	If the mobile application fulfills FR30, it shall be able to change the parameters based on which it automatically sends the GPS information upon request.
FR33	If the mobile application fulfills FR30, it shall implement authorization in server requests processing.
FR34	Mobile application may request and process track data between two specified positions from the server application.

## Connection establish
Communication between mobile and server applications will be done using a TCP connection. Mobile application will use SocketConnection class and establish a connection using open("socket://server:port "). It will then open input and output streams and keep the connection open. It will offer asynchronous and non-blocking communication interface for the rest of the application. In case of an error a listener will be called.
First message sent to the server identifies the mobile application. This will be used to identify the mobile application and the user working with it. Server application will respond with its identification, acknowledging the connection.
## Position sending
When configured, mobile application will send information retrieved from a GPS device to the server application in regular intervals. This will include current position, speed, altitude and course. Configuration will be done using common user interface.
Position information may be sent asynchronously as well, using defined interface method. If mobile application is not connected to the server, it will establish a connection.
## Buddy position requests
Mobile application can subscribe to receiving position information about other users. If the user data is available, server application will regularly send updates about subscribed users. Before other users can receive user information, he/she has to grant access to this data. This shall be allowed specifically for individual users or generally for all users.
## Parking tracking
Parking tracking allows to use a mobile phone as a tracking device, e.g. in vehicles. Before activating this function user has to enter parking position and maximum distance the phone can move away from the parking position. Once the phone stays out of this distance for more than 1 minute, it shall connect to the server and start sending its position in regular intervals. This shall be the same interval as for position sending requested by the user.
Position sending shall stop after the phone stays within the specified distance for more than 1 minute.
## Server commands
Server application may request current position and mobile application shall respond to this request.
Parking tracking shall be suspended after receiving an administrative command from the server application. Position sending shall be suspended for specified time interval. Tracking parameters may be updated by the server.
## Data format
Following text describes messages exchanged between mobile and server application.
### Special data types
Some messages data items will use variable data length. In such a case will be the item prefixed with its length, not counting the prefix itself. Length of the prefix is specified in the item type column in following tables.
### Connection establish
Protocol information – Connection establish (mobile)
Length	Type	Description
2 B	byte []	Header, fixed ASCII text: “CE”
1 B	byte	Mobile protocol version, fixed value: 1
15 B	byte []	IMEI, if known (as decimal number string)
variable	String	Login
variable	String	Password
2 B	short	Checksum

Server shall respond with CE message. Possible error codes: OK, AUTH_FAIL, VER_NSUPP, INV_CHKS, INV_DATA. Strings are 2-byte prefixed UTF-8 encoded strings.

Protocol information – Connection establish (server)
Length	Type	Description
2 B	byte []	Header, fixed ASCII text: “CE”
1 B	byte	Server protocol version, fixed value: 1
2 B	short	Checksum

In case of an error, mobile shall respond with MR message. Possible error codes: VER_NSUPP, INV_CHKS.
### Mobile information
Protocol information – Mobile information
Length	Type	Description
2 B	byte []	Header, fixed ASCII text: “MI”
4 B	int	Current latitude in degrees, multiplied by 100000
4 B	int	Current longitude in degrees, multiplied by 100000
2 B	short	Current speed in m/s, multiplied by 100
2 B	short	Current altitude in meters, multiplied by 100
2 B	short	Current course in degrees, multiplied by 100
2 B	short	Checksum

Server shall respond with SR message. Possible error codes: OK, INV_CHKS, INV_DATA.
### Mobile requests
Protocol information – Track user
Length	Type	Description
2 B	byte []	Header, fixed ASCII text: “TU”
1 B	byte	2 possible ASCII values: ‘1’ = start tracing, ‘0’ = stop tracing
variable	String	User name (his/her login)
2 B	short	Time interval in which information should be sent in seconds
2 B	short	Checksum

Server shall respond with SR message. Possible error codes: OK, INV_CHKS, INV_DATA, USR_NEX. Strings are 2-byte prefixed UTF-8 encoded strings.

Protocol information – Grant access
Length	Type	Description
2 B	byte []	Header, fixed ASCII text: “GA”
1 B	byte	Possible ASCII values: ‘3’ = grant access to all users, ‘2’ = grant access to specified user, ‘1’ = revoke access from specified user, ‘0’ = revoke access from all users
variable	String	User name (his/her login); / Value has no meaning unless previous item is set to ‘2’ or ‘1’
2 B	short	Checksum

Server shall respond with SR message. Possible error codes: OK, INV_CHKS, INV_DATA, USR_NEX. Strings are 2-byte prefixed UTF-8 encoded strings.

Protocol information – Are you alive
Length	Type	Description
2 B	byte []	Header, fixed ASCII text: “AA”
2 B	short	Checksum

Server shall respond with SR message. Possible error codes: OK, INV_CHKS.
Mobile application may use this message to keep the connection open.
### Server responses
Protocol information – Server response
Length	Type	Description
2 B	byte []	Header, fixed ASCII text: “SR”
2 B	short	Error code
2 B	short	Checksum

In case of an error, mobile shall respond with MR message. Possible error codes: INV_CHKS, INV_DATA.
### Server commands
Protocol information – Request position
Length	Type	Description
2 B	byte []	Header, fixed ASCII text: “RP”
2 B	short	Checksum

Mobile shall respond with MR message and followed by MI message if error code was OK. Possible error codes: OK, INV_CHKS, NO_DATA.

Protocol information – Stop parking tracking
Length	Type	Description
2 B	byte []	Header, fixed ASCII text: “ST”
variable	String	Parking password
4 B	int	Interval during which MI messages generated by parking tracking should not be sent, in seconds. Zero value means they should be sent again.
2 B	short	Checksum

Mobile shall respond with MR message. Possible error codes: OK, AUTH_FAIL, INV_CHKS, INV_DATA. Strings are 2-byte prefixed UTF-8 encoded strings.
Mobile application may close the connection after this command and reestablish a new one after specified time.

Protocol information – Change parking tracking parameters
Length	Type	Description
2 B	byte []	Header, fixed ASCII ext: “PT”
variable	String	Parking password
1 B	byte	ASCII values: ‘1’ = changing tracking activation, ‘0’ = no change
1 B	byte	ASCII values: ‘1’ = enable parking tracking, ‘0’ = disable parking tracking; / Value has no meaning unless previous item is set to ‘1’
1 B	String	ASCII values: ‘1’ = changing parking position, ‘0’ = no change
4 B	int	Parking position latitude in degrees, multiplied by 100000; / Value has no meaning unless previous item is set to ‘1’
4 B	int	Parking position longitude in degrees, multiplied by 100000; / Value has no meaning unless second to the previous item is set to ‘1’
1 B	String	ASCII values: ‘1’ = changing tracking distance, ‘0’ = no change
4 B	int	Parking tracking distance in meters; / Value has no meaning unless previous item is set to ‘1’
2 B	short	Checksum

Mobile shall respond with MR message. Possible error codes: OK, AUTH_FAIL, INV_CHKS, INV_DATA. Strings are 2-byte prefixed UTF-8 encoded strings.

Protocol information – Are you alive
Length	Type	Description
2 B	byte []	Header, fixed ASCII text: “AA”
2 B	short	Checksum

Mobile shall respond with MR message. Possible error codes: OK, INV_CHKS.
Server application may use this message to keep the connection open.

Protocol information – User information
Length	Type	Description
2 B	byte []	Header, fixed ASCII text: “UI”
variable	String	User name (his/her login)
4 B	int	User latitude in degrees, multiplied by 100000 and packed
4 B	int	User longitude in degrees, multiplied by 100000 and packed
2 B	short	User speed in m/s, multiplied by 100
2 B	short	User altitude in meters, multiplied by 100
2 B	short	User course in degrees, multiplied by 100
2 B	short	Checksum

Mobile shall respond with SR message. Possible error codes: OK, INV_CHKS, INV_DATA, USR_NEX. Strings are 2-byte prefixed UTF-8 encoded strings.
When the server application decides that user information is no longer valid, it will send all GPS information zeroed. This will indicate that no more updates will be sent and mobile application should try to subscribe to the data again. Same behavior will be applied in case the user will revoke access to his/her position.
### Mobile responses
Protocol information – Mobile response
Length	Type	Description
2 B	byte []	Header, fixed ASCII text: “MR”
2 B	short	Error code
2 B	short	Checksum

In case of an error, server shall respond with SR message. Possible error codes: INV_CHKS, INV_DATA.
### Server data
Server data messages will be sent after some mobile requests, e.g. requests for map or track data. These requests will be processed asynchronously, i.e. server will respond immediately with SR message and if its error code is OK it will be followed by a data message later.
Current version of mobile application will not request such data; these messages are reserved for future use.
### Checksum calculation
Checksum is calculated for all messages using CRC16 algorithm on the message data up to the checksum.
### Error codes
Protocol information – Error codes
Code	Name	Description	Sent after commands / Server Mobile
0	OK	OK	all	all
1	AUTH_FAIL	Authorization failure	CE, TU	ST, PT
2	VER_NSUPP	Protocol version not supported	CE	CE
3	MESG_NREC	Message type not recognized	all	all
4	INV_CHKS	Invalid checksum	all	all
5	INV_MESG	Invalid message format
6	INV_DATA	Invalid data	all	all
7	USR_NEX	User does not exist	TU	UI
8	NO_DATA	No data available	TU	RP

## Error handling
### Invalid data
Each side of the communication shall close the connection after sending 3 consecutive responses with error codes MESG_NREC or INV_CHKS. This will ensure that miscommunication between parties is resolved correctly. If the mobile application is not able to send at least one MI message in 3 consecutive connections it may decide to stop connecting to the server. Server application should notify the receivers in such a case.
### Inactivity
Each side of the communication may close the connection after 10 minutes since the last message was transferred. To keep the connection open AA messages may be sent. It is important to realize that mobile carriers can close connections after shorter time interval. Mobile application may detect that and send AA messages in interval shorter than detected maximum allowed inactivity time.
## Interfaces
Interface – ServerConnection
Method	Description	Parameters
ServerConnection		String login / String password / String objectName / ServerSettingsListener listener
connect
run
sendPosition	Send current position.
sendTraceRequest	Request tracing specified object.	String objectName
setTraceListener		TraceListener listener

Interface – TraceListener
Method	Description	Parameters
positionChanged	Called when new information about traced object is retrieved from the server.	int x / int y

Interface – ServerSettingsListener
Method	Description	Parameters
serverError		int errNo
serverSettingsChange		int type / int param

## Required configuration properties
Configuration properties – ServerConnection
Item	Description	Property
Name	Server name or IP address mobile application should connect to.	String serverName
Port	Server port number mobile application should connect to.	int serverPort
Login	User name used to authenticate to the server.	String login
Password	Password used to authenticate to the server.	String password
Interval	Non-zero value specifies interval in seconds in which information about current position shall be sent to the server (MI messages).	int interval
Parking tracking	Whether to track current position and start sending current position when moved away. / On/off value.	boolean parkingTracking
Parking password	Password for server commands related to parking tracking.	String parkingPassword
Parking position	Coordinates. It shall be possible to fill them in with the current position.	long parkingPositionX / long parkingPositionY
Trigger distance	Distance in meters from the parking position when the application should start sending its position.	long parkingTriggerDistance

# Communication with the desktop and other mobile devices (MDs)
## Overview
Desktop - MD and MD – MD communication will be used to exchange MaGeX data between the devices, namely maps, tracks and POIs.

Requirements
ID	Description	Remark
FR35	MDs shall be able to exchange tracks and POIs.
FR36	Only two MDs are involved in a MD – MD connection.
FR37	In a Desktop – MD connection, there will be 7 possible connections. Each connection requires a new instance of the desktop application and a different MD.
FR38	Each MD shall have a unique friendly name.	How to enforce this rule?
FR39	Referring to FR43, the MD Bluetooth client shall by default try to establish a connection to the last Bluetooth server it was connected to.

## Connection establish – Bluetooth server
### Abstract description
The user pressed a button in the menu of a MD with the intention of sharing MaGeX data with another MD and wanting to control the transport of data with the MD. The MD will initiate a Bluetooth server and wait for incoming connections. Duration of this period is not limited, the user can press the “Cancel” button, thereby terminating the server and returning to the menu. If a client connects to the server, it will display a “file manager”-like menu, where POIs and tracks can be shared. After data sharing is finished, the user presses the “Disconnect” button and is return to the application menu.

### Technical description
BtServerManager class will be responsible for the common routine of setting up a Bluetooth server. The design pattern singleton will be used.
The Bluetooth server will be set to DiscoveryAgent.GIAC mode via setDiscoverable method. Then it will use the StreamConnection class with the server url btspp://localhost:uuid;authenticate=false;authorize=false. After opening the connection, the service record will be modified to contain the correct device class, service availability, service name and service description. Then the blocking method acceptAndOpen() will be invoked in a new thread to avoid blocking and the application will wait for a client to connect. The uuid and service record attribute being used are defined below. If a client wishes to connect, an InputStream and OutputStream will be opened and the connection will be established.

## Connection establishment – Bluetooth client
### Abstract description
(poznamka – passive state -> nic s telefonom nerobit, active state -> normalne pracujes s aplikaciou … zakomponovat to do popisu, alebo je to “jasne”?)
The user pressed a button in the menu of a MD with the intention of sharing MaGeX data with another MD or desktop. The MD will try to connect to the default device. If there is not default device or the default device cannot be found, a list of devices to which the user can connect will appear on the display. After choosing which device to connect to, the MD will connect to that device, enter a passive state and wait for the termination of the connection from the server or by pressing the button “Cancel”. After the connection is severed, the MD will return from its passive state into the active state.
### Technical description
BtClientManager class will be responsible for the common routine of connecting to a Bluetooth server. The design pattern singleton will be used.
Using the DiscoveryListener interface the surrounding Bluetooth devices will be discovered by calling the method startInquiry(DiscoveryAgent.GIAC,this). The devices discovered in deviceDiscovered(RemoteDevice btDevice,DeviceClass cod) will be stored in a Vector. In case it finds a default device, it tries to connect automatically to the MaGeX service via a default service record. If not, those devices will be immediately searched for the MaGeX service. After the service search is finished, the client will call the presenceFound method with the friendlyNames parameter (servers, shown by device friendly name that can be connected to).. The client may allow the user to see the attributes of the server. If the user chooses to connect to a server, a ConnectionURL will be retrieved from the server’s service record with the method getConnectionURL().As with the server url, the parameter will be ServiceRecord.NOAUTHENTICATE_NOENCRYPT. With the connection opened by the open(url) method in StreamConnection class, an InputStream and OutputStream will be opened and the connection will be established.

## Interfaces

Interface – BtConnectionListener
Method	Description	Parameters / Return value
presenceFound	Returns list of potential servers (their friendly name) for the client MD. Returns the friendly name of the connected client for the server MD.	String[] friendlyNames / -
connected	The method is called when a connection is established.	- / -
errorMessage	The Bluetooth manager class has experienced an error in the connection and notifies it.	int errorCode / -
disconnected	Notifies that the device is no longer connected to the friendlyName device.	String friendlyName / -
dataReceived	Notifies that a new MapObject has been received and make it available as a parameter.	MapObject mObject / / -

Constants
Type	Value	Name	Description
Protocol signals	0 REQUESTING_MAPOBJECT Bluetooth server is requesting a MapObject / 1 SENDING_MAPOBJECT The specified MapObject name is already being used. / 3 MAPOBJECT_NOT_FOUND The MapObject with the specified name does not exist.

## Classes
These are the main classes that will be used. Only the methods that should be used by the menu class(es) are listed.

Interface – BtClientManager
Method	Description	Parameters / Return value
getInstance	Returns the instance of the class.	- / BtClientManager instance
run	Inherited from the Runnable interface. This method starts the client.	- / -
terminateConnection	Tries to terminate the connection with the friendlyName server.	String friendlyName/ -
sendData	Sends the MapObject identified by dataID to the other MD.	String dataID, byte dataType / -
connectToSpecified	Tries to connect to the friendlyName server.	String friendlyName

Interface – BtServerManager
Method	Description	Parameters / Return value
getInstance	Returns the instance of the class.	- / BtServerManager instance
run	Inherited from the Runnable interface. This method starts the server.	- / -
terminateConnection	Tries to terminate the connection with the friendlyName server.	String friendlyName/ -
sendData	Sends the MapObject identified by dataID to the other MD.	String dataID / -
getData	Gets the MapObject identified by dataID to the other MD.	String dataID / -

## Data selection
The MDs can send tracks and POIs between each other. Maps can be shared only between a MD and the desktop. Even this data sharing is limited, because maps cannot be saved inside the JAR without repacking, which cannot be done on the MD during the application’s usage. Therefore map will be store solely in the RMS of the MD. The desktop does not have these limitations.

## Communication protocol
After sendData method is called the MapObject, identified by dataID,
 will be serialized and sent through the OutputStream to the other device where it will be de-serialized. Serialization means that each member of MapObject will be written into a DataOutputStream, which will be fed into the InputStream as a byte array. De-serialization is the opposite: a DataInputStream will be instantiated from the InputStream and the MapObject members will be stored in a new MapObject. The order of the members being serialized is not important, as long as they are serialized and de-serialized in the same order.
Before each MapObject is sent, the corresponding protocol signal is sent to notify the device of the transmitting of data.
When a server requests a MapObject it will first sent the corresponding protocol signal follow by the dataID. If the MapObject is not found on the client side, the signal MAPOBJECT_NOT_FOUND will be sent back.
## Post-processing
After the de-serialization of MapObject members into a new MapObject instance, the dataRetrieved method is called and the menu class does what is necessary (saves the data, for example).
If MapObject instance is null, this means that the requested MapObject was not found on the other device.
## Required configuration properties

Configuration properties – BtConnectionListener
Item	Description	Property
UUID	The UUID of the MaGeX Bluetooth service.	String UUID
Service Name	Name of the MaGeX service.	String serviceName
Service Description	Describes the use of the MaGeX service.	String serviceDesc

# User Interaction
## Vector map display
### Overview
All active (activated by user) data stored in application (RMS or JAR) shall be displayed. If GPS module is active and in AVAILABLE state, application shall display current position in the center of the map. Position can be frozen and user shall be able to browse map. If GPS module is disabled, application shall act only as a browser of maps.

Requirements
ID	Description	Remark
FR40	Mobile application shall be able to display all map information stored by the application. See chapter 3 for the list of map object types.
FR41	Mobile application shall display user’s current position returned by a GPS module on a map.
FR42	When the position changes, the application shall move the map so the user’s position is always in the center of the screen.
FR43	If GPS module is not active (or simply is not found), application shall display static map, which can be browsed by cursor.
FR44	Mobile application shall be able to display meridians and parallels and their values.
FR45	User shall be informed before changing of map level if will use zoom. (All data are loaded newly.)
FR46	Invisible data (data outside map) must be ignored.

Interface – MapManager
Method	Description	Parameters / Return value
drawPoi	Draws point of interest with its specifics.	Poi poi
drawPolyline	Draws polyline with its specifics.	Polyline polyline
drawPolygon	Draws polygon with its specifics.	Polygon polygon
drawCoordLines	Draw coordinates and their values.
startTrackRecord	Starts with new track recording. Only one track can be recorded at one time.
stopTrackRecord	Stops recording a track. Calls dialog to specify track label etc.
showWaypoint	Show position of waypoint on the map..	Waypoint waypoint
showPosition	Show position on the map.	Coord coord

### Displaying points of interest
Every type of poi has its own mark (image or icon) and (almost)every poi has own label. This information shall be displayed depending on setting. Next criterion is zoom of map. In some zooms are displayed only some pois (it is due to better transparency of map).

Requirements
ID	Description	Remark
FR47	User shall be allowed to specify which of the POIs returned by a search should be displayed.
FR48	Displaying of poi shall depend on map zoom.
FR49	If poi elevation is specified, it shall be displayed behind label.
FR50	Every point of interest shall have its own icon.
FR51	Pois shall be drawn after polygons and polylines and before tracks and waypoints.

### Displaying polylines
Polylines are displayed depending on their type. Specific line is for all types of polyline. Label of polyline is drawn to specific position.

Requirements
ID	Description	Remark
FR52	Every type of polyline shall have its line type and line color.
FR53	If label is specified, application shall display label to specific (counted on creating polyline) position.
FR54	Labels of some types (such a number of road) of polylines shall be drawn with its background.
FR55	Polylines shall be drawn after polygons and before pois, tracks and waypoints.

### Displaying polygons
Polygon shall be drawn in two modes. Standard mode means that polygon shall be filled. Special mode means, that only periphery line shall be drawn (such as polyline with specific color). Polygons shall be filled by method, which shall allow fast filling. (Methods: library – JmicroPolygon, JSR 184, other(?) - depends on their speed – it will be tested).
Requirements
ID	Description	Remark
FR56	Every type of polygon shall have its specific color (color can be same for similar types).
FR57	If label is specified, application shall display label to specific (counted on creating polygon) position.
FR58	Two modes of drawing polygons – filling or drawing periphery line.
FR59	Polygons shall be drawn before polylines, pois, tracks and waypoints.

## Waypoints and tracks
### Overview
Requirements
ID	Description	Remark
FR60	Mobile application shall display stored waypoints in a map.
FR61	Mobile application shall display selected stored tracks in a map.
FR62	Mobile application shall allow the user to browse the list of stored waypoints and select waypoint to be displayed on the map.
FR63	Mobile application shall allow the user to browse the list of stored tracks and select tracks to be displayed with the map data.
FR64	Mobile application shall allow display information for waypoint specified in list of waypoints.
FR65	Mobile application shall allow display information for track specified in list of tracks.
FR66	Switching navigation to the next waypoint in the track shall be done automatically once the current position is within predefined distance from the waypoint. Apart from this, user should be allowed to manually skip to the next waypoint and to return to the previous one.
FR67	During the navigation, mobile application shall display the distance to the end of selected track. The distance shall be calculated as a distance to the selected waypoint and a distance between the next waypoints in the track.
FR68	Mobile application may use sound or voice to provide the user with navigation commands or information about the track.

### Display
Tracks and waypoints shall be drawn as pois or polyline. Their displaying shall be flashy (to recognize these special types). It shall be possible to display non static waypoints – this means, that these points shall change their position by the time. (Position of another machine.)

Requirements
ID	Description	Remark
FR69	Track or waypoint shall be displayed flashy.
FR70	Waypoints shall be drawn after polygons, polylines, pois and tracks.
FR71	Tracks shall be drawn after polygons, polylines, pois and before waypoints.
FR72	Waypoint shall be drawn with icon of its type.
FR73	Track shall be drawn with specific line (???).

### Track creation
User shall be able to record his track (his moving). He shall create the track by start recording at beginning and stop at finish point. This track shall be stored and shall be able to be described by user. User should create track by clicking on the map and creating points of track.

Requirements
ID	Description	Remark
FR74	Mobile application shall allow user to record his moving by creating track.
FR75	Track shall be recorded after user shall start it.
FR76	User shall be able to stop recording at any time.
FR77	User shall be able to specify track description before saving.
FR78	Track should be created by clicking points on the map.

## Navigation
### Overview
Two methods of navigating shall be implemented. Navigation to the point and along the track. Navigation shall be able to use stored waypoint, point of interest, or any other clicked point on the map. Second method shall use stored track (that means, that track must be created before navigation). And then navigation is similar to first method.

Requirements
ID	Description	Remark
FR79	Application shall navigate user to the specific point. (waypoint, point of interest, clicked point on the map)
FR80	Application shall navigate user ton the stored track.
FR81	User shall choose waypoint to navigation from list of waypoints.
FR82	User shall be able to click on the map to create navigation point.
FR83	User shall choose track to navigation from list of tracks.
FR84	Navigation shall include displaying azimuth and distance to the waypoint.

### Navigation to the point

Requirements
ID	Description	Remark
FR85	Application shall navigate user to the specific point. (waypoint, point of interest, clicked point on the map)
FR86	Application shall navigate user ton the stored track.
FR87	User shall choose waypoint to navigation from list of waypoints.

### Navigation along the track
Navigation starts with navigating to the first point. Navigation to the next point (on the track) shall be switched if user reach previous point (or its surrounding) or next point will be nearer.
Requirements
ID	Description	Remark
FR88	Mobile application shall navigate user along the selected track. This shall be done by navigating to the first point in the track and once the point is reached, switch to the next point.
FR89	Switching navigation to the next waypoint in the track shall be done automatically once the current position is within predefined distance from the waypoint. Apart from this, user should be allowed to manually skip to the next waypoint and to return to the previous one.
FR90	During the navigation, mobile application shall display the distance to the end of selected track. The distance shall be calculated as a distance to the selected waypoint and a distance between the next waypoints in the track.
FR91	Mobile application may use sound or voice to provide the user with navigation commands or information about the track.

### Required configuration properties
Configuration properties – GPSProvider
Item	Description	Property
Track waypoint switch distance

## Searching
### Overview
Mobile application shall allow user to search objects on the maps which are stored in application. Objects are searched by name or by position (or both). For position there is surrounding where object shall be looking for.

Requirements
ID	Description	Remark
FR92	Mobile application shall allow user to search for cities, streets and other named objects stored in maps.
FR93	Object search shall be performed on name, type, position or a combination of these attributes.
FR94	Object search position shall be specified as coordinates or as a maximum distance from specified coordinates. Coordinated shall be specified by a WGS84 value, cursor position on a map or by current position returned by a GPS module.
FR95	Object shall be looking for only in active maps.

### Possibilities of searching
User shall specify, which objects will be searched or where (in which distance) object will be searched.

Requirements
ID	Description	Remark
FR96	It shall be possible to specify types of objects which will be in result of searching.
FR97	It shall be possible to specify group of objects which will be in result of searching. For example only cities or sightseeings etc.
FR98	Distance from coordination shall be able to set.

## Application screens
### Overview
This part summarizes all interfaces which user shall see and use while working with application. There shall be two modes – map and menu. After switching on the app, map shall be displayed.

Requirements
ID	Description	Remark
FR99	Map – displays all geographical data
FR100	Data manager – displays lists of stored objects
FR101	Search manager – displays form for searching, stores set parameters etc.
FR102	Configuration manager – displays form for setting application and provides saving of these data.
FR103	GPS info viewer – displays available data from GPS and others.
FR104	Help – information about application and others.

### Map
Map Manager shall be used for displaying map.

Requirements
ID	Description	Remark
FR105	Shall show all active maps.
FR106	Shall show tracks and waypoints.
FR107	Shall show geographical coordinates.
FR108	Shall show current position (point and coordinates).
FR109	Shall show some basic info from GPS.
FR110	User shall be able to move with cursor on the map, creates tracks or set navigation point.
FR111	Map shall allow to choose mode.

### Data manager
Data manager shall manage all map data. Data shall be able to be deleted, renamed or send to another user. Manager shall provide communication (high level communication) with desktop.

Requirements
ID	Description	Remark
FR112	Shall show all available maps in app. Shall allow to mark or unmark map, delete map or to show info about map.
FR113	Shall show all available tracks in app. Shall allow to mark or unmark track, delete track, show info about track, navigate along track or send track to another user.
FR114	Shall show all available waypoints in app. Shall allow to mark or unmark waypoint, delete waypoint, show info about waypoint, navigate to the waypoint or send waypoint to another user.
FR115	Shall allow desktop application to gain access to the phone.

### Search manager
Shall provide high level searching of objects stored in mobile application.

Requirements
ID	Description	Remark
FR116	Shall show searching form.
FR117	Shall show setting form for specify searching objects or distance from position.
FR118	Shall show list of results, where user shall choose and display object on the map.

### Configuration manager
All settings shall be stored in one RMS database. Manager of this database shall have two types of methods get and set. These types shall be for all settings which user shall be able to use.

Requirements
ID	Description	Remark
FR119	Shall show all settings.
FR120	Shall provide storing all configuration into RMS and loading it.
FR121	Shall contain map display mode setting.
FR122	Shall contain „objects to search“ configuration.
FR123	Shall contain polygon mode setting.
FR124	Shall contain language setting.
FR125	Shall contain server setting.

Interface – ConfigurationManager
Method	Description	Parameters / Return value
ConfigurationManager	Constructor
getMapDisplayMode	Returns if day or night mode is set.	/ byte
setMapDisplayMode	Sets day / night mode	byte mode
getDispalyingPois	Returns bitmap of types of pois.	/bitmap
setDisplayingPois	Sets which types of pois will be displayed.	bitmap
getObjectsToSearch	Returns bitmap of objects which will be in result of searching.	/bitmap
setObjectsToSearch	Sets objects which will be in result of searching	bitmap
getPolygonMode	Returns mode in which polygon will be drawn.	/ boolean
setPolygonMode	Sets how polygon will be drawn.	boolean mode
getLanguage	Returns which language is set.	/ byte
setLanguage	Sets language.	byte language

Interface – Constants
Type	Value	Name	Description
int	0 DISPLAY_MODE_DAY Map colors – light background / 1 DISPLAY_MODE_NIGHT Map colors – dark background / 0 POLYGON_MODE_FILL Drawing polygons - filling / 1 POLYGON_MODE_PERIPHERY Drawing polygons – periphery line drawing / 0 LANGUAGE_EN / 1 LANGUAGE_CZ / 2 LANGUAGE_SK / 3 LANGUAGE_DE

### GPS info viewer

Requirements
ID	Description	Remark
FR126	Shall show basic information available from GPS.
FR127	Shall show extended information available from GPS.
FR128	Shall show information about current track.
FR129	Should show other information such as sunset or sunrise.

### Help

Requirements
ID	Description	Remark
FR130	How to control application.
FR131	Information about project.
FR132	Authors.
FR133	License.

## Dictionary

Active maps – maps which are set as visible on the display.
Zoom – which details map will display
Level – one of three or four parts of map, these parts cover same area, but with another details

point – consists only of coordinations (in app as Coord)

Poi – point of interest – one point as part of map (point and info)
Polyline – 1D object of the map (vector of points and info)
Polygon – 2D object of the map (vector of points and info)

Map – consists of Pois, Polylines, Polygons

Waypoint – object created by user, similar to Poi but contains more information
Track – object created by user, similar to polyline, but contains more information

# Document History
Document Name	Requirements and Design: Mobile Application
Version	0.2
Changes History	Version Author Date / 0.1 Rastislav Wartiak, Ondřej Dušek, Nguyen Son Tung, Martin Kontsek, David Stach 20.3.2008 / 0.2 Rastislav Wartiak 24.3.2008 / 0.2 Ondřej Dušek 27.3.2008